## Slide 1: Discontinuity Edge Overdraw
Pedro V. Sander1
Hugues Hoppe2
John Snyder2
Steven J. Gortler1
2001 ACM Symposium on Interactive 3D Graphics
1 Harvard University 2 Microsoft Research

## Slide 2: Aliasing in meshes
  Within triangles interiors (solved by mipmapping)
  Among triangles (‘small object problem’)
  At triangle edges (‘crawling jaggies’)
Notes: There are three types of aliasing in meshes.
There is aliasing within triangle interiors.
This is solved by mipmapping when the model is texture-mapped.
Then there is the small object problem. If the mesh is very far away, and the same pixel owns several triangles, all bets are off as to which triangle will shade that pixel.
There is also aliasing at triangle edges. The so called crawling jaggies. Sort of like a staircase effect that is noticeable at material boundaries and silhouettes. This becomes even more noticeable and crawls as the model moves.
This paper focuses on attempting to remove aliasing at triangle edges.

## Slide 3: Our approach: only attack jaggies
Basic algorithm:
  Render mesh.
  Identify ‘troublesome’ edges.
  Render troublesome edges as antialiased lines.
Original
Overdrawn Edges
Final Result
+
=
Notes: Our approach is to only attack the jaggies.
First we render the mesh.
Then we identify the troublesome edges that cause the jaggies.
Then we render all the troublesome edges as antialiased lines.
This yields the final antialiased result shown on the right.

## Slide 4: Edge overdraw demo
Notes: So here are a couple of demos of edge overdraw.
I wjll now toggle overdraw on and off…

## Slide 5: Previous work: Supersampling
In the limit, solves all aliasing artifacts.
However, higher rendering cost.
e.g. 2x2:
Method | Transform | Raster | Memory
Traditional Supersampling | 1x | 4x | 4x
Accumulation Buffer | 4x | 4x | 2x
Notes: At the limit, supersampling solves all aliasing artifacts. But today’s hardware usually allows us to do 2x2 supersampling (maybe 4x4 at most).
2x2 supersampling helps covering the artifacts, but at a very high cost.
Traditional 2x2 Supersampling requires a frame buffer that is 4 times as big, and has a rasterization cost 4 times larger than the regular rasterization cost.
Accumulation buffer renders the frame four times to an auxiliary buffer, each time using different samples, while averaging the result into the frame buffer. So it doesn’t have the same memory overhead, but it has to transform the geometry four times. [sure?]
[maybe mention polygon aa on opengl that requires sorting]

## Slide 6: Previous work: Edge Antialiasing
Crow ‘77 Scanline renderer
Bloomenthal ‘83 Image post-process
OpenGL “polygon antialiasing” Requires special hardware & front-to-back rendering

## Slide 7: Previous work: edge overdraw
Sauer et al ‘99 2-pass software rendering. Requires polygon sorting. Only silhouettes & brute-force search.
Wimmer ‘97 Requires polygon sorting.
Donovan ‘99 framebuffer-to-texture copy

## Slide 8: Our contribution
Use ordinary line antialiasing.
Reduce crawling jaggies, while maintaining:
  Temporal smoothness
  Spatial consistency
  Spatial sharpness
Fast detection of discontinuity edges
Notes: Careful exploration of details

## Slide 9: Discontinuity edges
Dynamic discontinuity edges
  Silhouette edges
Static discontinuity edges (“sharp edges”)
  Surface boundaries
  Material boundaries
  Creases
Notes: The crawling jaggies occur at Discontinuity edges.
What are discontinuity edges?
The edges on the silhouette of the model are dynamic discontinuity edges, since they depend on the current viewpoint.
The static discontinuity edges, which we will call “sharp edges” can be split up into three categories.
Surface boundaries are edges that are at the extremes of the mesh. They have only a single adjacent face [explain better?]

## Slide 10: Discontinuity edges
Dynamic discontinuity edges
  Silhouette edges
Static discontinuity edges (“sharp edges”)
  Surface boundaries
  Material boundaries
  Creases
Notes: Material boundaries are edges in which the adjacent faces have different material properties, like a different color, or a different texture. For instance, note the sudden change in color in the model’s shirt from blue to yellow.

## Slide 11: Discontinuity edges
Dynamic discontinuity edges
  Silhouette edges
Static discontinuity edges (“sharp edges”)
  Surface boundaries
  Material boundaries
  Creases
Notes: Creases are edges that present normal discontinuities. Note the arm of the model.

## Slide 12: Silhouette extraction
[Sander et al 2000] Build silhouette tree during preprocess. Each node contains:
  Set of edges.
  Conservative test.
If test passes, then sub-tree is skipped.
Notes: In order to overdraw the silhouette edges, first we need an efficient way of detecting them.
So for silhouette extraction, we use the algorithm we presented in the Silhouette Clipping paper at last year’s siggraph.
We build a silhouette extraction hierarchy during the preprocessing phase.
The edges are arranged hierarchically in a tree.
Then, at runtime we can apply a quick conservative test at each node of the tree.
If the test passes, we know that, for the current viewpoint, none of the edges associated with that node and descendent nodes can be in the silhouette.

## Slide 13: Silhouette extraction tree
Leave out:
  Sharp edges (~10%)
  Concave edges (~40%)
Reduces silhouette extraction cost by half.
Notes: Note that we don’t have to consider the sharp edges when building the silhouette tree. That’s because they are discontinuity edges anyway, so they will have to be overdrawn in all frames regardless of the viewpoint.
Also note that, if we have a closed mesh, concave edges need not be in the tree either. All concave silhouette edges are not visible. Again, that’s assuming the mesh is closed. In a bumpy model, almost half the edges tend to be concave.
So, that can cut the silhouette extraction cost by half.

## Slide 14: Shading the edges
Silhouette edge: Use the frontface shading attributes.
Frontfacing edge: Combine between the two face shading attributes (avoids popping).
Popping
Notes: Now how do we shade the edges?
For silhouette edges, we use the frontface shading attributes when rendering the antialiased line. So we use the attributes of the geed face.
Notice that, at some point, the green face might become a backface of that silhouette edge. At that time we will need to be using the red face’s attributes to shade the edge.
If this transition occurs suddenly, we will get a popping artifact.
Therefore when the edge is frontfacing, we combine the attributes of the two faces.
It the edge is frontfacing, then we need to combine the shading attributes of the two faces. If we just used the shading attributes of one face, there would be a noticeable “pop” when the edge becomes a silhouette edge, since that could change the shading attributes of the edge if the default face becomes backfacing. [explain better?]

## Slide 15: Temporal smoothness: sharp edge combining
d1 = dot(e.f1,viewdir)
d2 = dot(e.f2,viewdir)
β = d1 / (d1 + d2)
Combining
Popping
Notes: To achieve this combining, we compute a dot product between each face normal and the view direction, and then we compute an associated combining weight beta.
The face whose orientation is “more” frontfacing yields a higher dot product.
These dot products determine the amount of contribution from each face to the rendering of the edge.

## Slide 16: How to combine
Two approaches:
Edge blended-draw
  Blend face attributes and render once.
  Catches occasional highlight.
  Requires multitexturing.
Edge double-draw
  Render twice (once for each face’s attributes).
  Requires rendering more edges.
  Causes slight discontinuity at β==0.5
Notes: In order to combine the edges, we have explored two approaches: edge blended-draw and edge double-draw.
In edge blended-draw, we blend the material attributes and then render the edge once. One problem with blended draw is that the interpolated surface normal can produce incorrect highlights. For textured models, this method also requires multitexturing.
Edge double-draw avoids these problems by rendering the edge twice, once for each of the faces’ material attributes.
This requires rendering a larger number of edges per frame.
As described in the paper, the edge with the highest dot product has to be rendered first. This causes a slight discontinuity at beta = .5. We found it to be imperceptible.

## Slide 17: Drawbacks of combining
Slower.
Blurs discontinuities too much.
Combined
Asymmetric Combination
Original
Notes: Lets look at the drawbacks of this combining approach.
First it is slower, because the material attributes have to be combined.
Second it blurs discontinuities too much, as evidenced in the center picture. It adds an antialiased line whose color is different than both adjacent faces colors’.
Note, on the right, that the result looks much sharper. We will now show how we achieve that.

## Slide 18: Spatial sharpness: asymmetric edge combining
We combine as little as possible.
We use an asymmetric ramp.
Most of the time use “default” face.
.9
1.0
0
0
1.0
Symmetric β
Asymmetric β
Notes: To accomplish this, we propose combining as little as possible. We do that by using an asymmetric ramp.
Most of the time, we use the attributes of a default face, and when that face is very close to becoming backfacing, then we start combining. That reduces the number of edges that need to be overdrawn, since fewer edges need to be combined.

## Slide 19: Sharp edge orientation
For each edge, determine a default face.
Consistent through sharp edge paths.
Not consistent
Consistent
Notes: Since our approach usually renders an edge using a chosen default face, we need to be consistent when assigning face attributes along sharp edge paths.
Take a look at the undesired artifacts on the left if no consistent orientation is chosen.

## Slide 20: Spatial consistency: sharp edge orientation
Traverse sharp edge paths setting consistent edge orientation. Stops at:
  Dead ends
  Loop
  Multiple sharp edge “crossings”
Notes: We orient the edges with a simple heuristic. It is a very fast linear-time operation.
We just traverse all sharp edge paths setting a consistent orientation.
The sharp edge paths of the plane model are highlighted in blue.
A path is a sequence of sharp edges. The path stops, when you reach a dead end (like at the end of the plane’s wing), when it loops back to the beginning, (like in the plane windows), or at crossings of more than two sharp edges.

## Slide 21: Discontinuity edge sorting
For best results, sort edges from back to front.
No need to sort edges that are far from the silhouette.
Not sorted
Sorted
Notes: In order to get correct semi-transparency, we need to sort the edges from back to front.
We only have to do this with silhouette edges and edges near silhouettes. The other edges will be completely overdrawn over their adjacent faces so they don’t need to be sorted and can be rendered first. [explain better]

## Slide 22: Sorting demo
Notes: Now I will present a demo that shows the advantage of sorting.
Note the edge shimmering…
This is an optional step. In many smooth organic models, sorting is not necessary like the dinosaur example I will show now.

## Slide 23: Final algorithm (Preprocess)
Collect sharp edges in mesh.
Assign them consistent orientation.
Construct silhouette extraction tree (exclude sharp and concave edges).
Notes: Now lets go through the entire algorithm.
During preprocess,
first we must collect all the sharp edges in the mesh and assign consistent orientations to them.
Then we construct the silhouette extraction tree.
This is by far the most time consuming step. It takes several minutes for large meshes.

## Slide 24: Final algorithm (Runtime)
render mesh;
extract silhouette;
for silhouette edge e
render e using frontface shading attributes
for sharp edge e
compute e.β;
if e.β < 0.9 then
render e using default face shading attributes
else
render e by combining shading attributes
Notes: Then at runtime,
We first render the mesh.
Then we extract the silhouette edges.
Then we render the silhouette edges using the frontface shading attributes.
Then for every sharp edge, we compute the dot products and subsequently the edge’s beta value.
The beta is less than 0.9, then we can render the edge using the attributes of the default face.
Otherwise, the default face is close to being backfacing, and to avoid popping, we combine the material attributes of the two faces using beta.

## Slide 25: Final algorithm (modifications for sorting)
Render sharp edges for which 0.1 < e.β < 0.9
Place other sharp edges in a set S.
Place silhouette edges in S.
Sort S back-to-front.
Render edges in S.
Notes: In the case of sorting.
First we render the sharp edges that are “far” from being in the silhouette.
Then we place the other sharp edges and the silhouette edges in a set S.
Then we sort S back to front.
Finally we render the edges in S in sorted order.

## Slide 26: Rendering Details
Render triangles:
  standard z-buffer settings.
  GL_POLYGON_OFFSET_FILL.
Render edges (as antialiased lines):
  OVER operation.
  z-buffer writes disabled.
Notes: Now let me discuss a couple of rendering details.
When rendering the model, we using the standard Z-buffer settings.
We enable GL_POLYGON_OFFSET_FILL to perturb the z-buffer values of triangles behind those of lines.
When rendering the edges, we turn off z-buffer writes to prevent gaps between chains of antialised edges. Note that we still check the z-buffer when rendering the edges, we just disable writing to it.

## Slide 27: Timings
Model | Dino | Plane | Man | Ship
Faces | 43,866 | 8,000 | 1,586 | 85,068
Edges | 65,799 | 12,000 | 2,379 | 127,602
Sharp edges | 900 | 2,085 | 354 | 19,769
Notes: Now I will show some timing results for these four models. Note that the dino has a small fraction of sharp edges, while the ship has a lot of sharp edges.

## Slide 28: Timings
Model | Dino | Plane | Man | Ship
Faces | 43,866 | 8,000 | 1,586 | 85,068
Edges | 65,799 | 12,000 | 2,379 | 127,602
Sharp edges | 900 | 2,085 | 354 | 19,769
Edge stats averaged over 100 viewpoints |  |  |  | 
Extracted Sil edges | 2,086 | 393 | 94 | 7,122
Rendered edges | 2,681 | 1,727 | 373 | 21,980
Sorted edges | 2,288 | 1,212 | 309 | 16,448
Combined edges | 12 | 23 | 6 | 266
Notes: These are some stats averaged over 100 viewpoints.
Note that the number of edges that require combining is usually very small.

## Slide 29: Timings
Model | Dino | Plane | Man | Ship
Faces | 43,866 | 8,000 | 1,586 | 85,068
Edges | 65,799 | 12,000 | 2,379 | 127,602
Sharp edges | 900 | 2,085 | 354 | 19,769
Edge stats averaged over 100 viewpoints |  |  |  | 
Extracted Sil edges | 2,086 | 393 | 94 | 7,122
Rendered edges | 2,681 | 1,727 | 373 | 21,980
Sorted edges | 2,288 | 1,212 | 309 | 16,448
Combined edges | 12 | 23 | 6 | 266
Rendering time per frame (in milliseconds) |  |  |  | 
No Edge Overdraw | 18.9 | 9.8 | 7.2 | 40.1
Edge Overdraw | 20.0 | 10.3 | 7.7 | 88.4
Sorted Edge Overdraw | 23.3 | 10.8 | 7.7 | 121.2
Pentium III 800Mhz, GeForce2
Notes: Note that the time overhead for overdrawing the edges is also small, becoming a bit larger when sorting.
There is one exception, which is the ship. While our algorithm antialiases the model very nicely, the ship has a very high proportion of sharp edges. That makes the edge overdraw technique much slower.

## Slide 30: Comparison with Supersampling
Original
2x2 Supersampled
Overdraw
(explicit geometry of antialiased lines gives better coverage information)
Notes: Here we compare the original rendering, with the 2x2 supersampled one. Note that the jaggies are much less evident, but still present. Note that our method based on line antialising, shown on the right, does a better job hiding those evil jaggies.

## Slide 31
Original
Sorted Overdraw
Notes: Here we show some comparisons between the original rendering and edge overdraw.
Note that edge overdraw bloats the model a bit, which is most evident on the man example on the right.

## Slide 32: Demos
Notes: Now I will show some demos of Edge Overdraw.
[man demo instead of para]

## Slide 33: Limitations
It ‘thickens’ the model a bit (mostly visible at low resolutions).
Memory overhead.
Original
Overdraw
Notes: The main limitation of our algorithm is the fact that it thickens the model a bit. That is most visible at low resolutions.
There is also a memory overhead, mainly due to the silhouette extraction tree. The overhead is comparable to storing a mesh using a data structure with connectivity information.

## Slide 34: Summary
Edge overdraw is a simple, efficient alternative for eliminating jaggies.
Designed to reduce spatial aliasing.
But, also reduces crawling jaggies.
Future work: Extracting silhouettes on dynamic meshes.
Notes: We introduced Discontinuity Edge Overdraw, a simple technique to eliminate the crawling jaggies.
The technique was designed to remove spatial aliasing.
And it does a good job specially at removing spatial aliasing of the crawling kind, that is, over time.
The technique was tested in generic PC graphics cards, and an SGI workstation. It does not require specialized hardware.
An interesting area of future work would be on developing an algorithm to efficiently extract the silhouette edges of dynamic meshes.
Additional things not in talk yet: Can we compare with NVIDIA GeForce 3 “multisampling”?
The random vector to pick default face

## Slide 35: The end